## Slide 1: Future of Wind Turbines and Viewsheds: A quantitative Approach
Open-Source Python library for Visual Impact Assessment (VIA) of Onshore Wind Turbine Projects
Chinna Subbaraya Siddharth Ramavajjala, MSc Cartography and GIS, Dept of Geography

## Slide 2: Overview
Introduction (Problem Statement)
The Problem
The Solution
GIS Workflow
Live Demo
Future work
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography

## Slide 3: Introduction
Wind power continues to be one of the fastest growing and lowest-cost sources of electricity in the US (DoE 2023)
Large-scale onshore wind projects has a visual impact on our landscapes.
Conflicts scenic quality and visual aesthetics
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 4: Key terms
Distance Zone: Effect of distance on how a turbine is perceived
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography
Turbine-1
Turbine-2
Turbine-3
Turbine-1
Turbine-2
Turbine-3
Increasing Distance from observer

## Slide 5: Key terms
Visual Exposure: The amount of turbine visible to observer at a relative height
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography
Blade End Visibility
Hub Visibility
Rotor Sweep Visibility

## Slide 6: Key terms
Turbine Visual Prominence means “How prominent a turbine is”
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography
Turbine-1 Turbine-2 Turbine-3
Turbine-1
Turbine-2
Scenario-1
Scenario-2

## Slide 7: The Problem
Visual Impact Assessment (VIA) crucial and mandated as part of permitting process. (Shadow Flicker and Noise)
Without VIA or with flawed VIA can lead to sub-optimal site selection for wind projects
No open-source Python tools available to perform VIA except GRASS GIS
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography

## Slide 8: The Solution
To develop an open-source Python library viawind*
Python library that abstracts VIA geospatial workflow to a simple methods and performs
The library has to support visualization of geospatial data products and allow users to interact with outputs.
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography

## Slide 9
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Shapely
(Palmer 2022)
Raster Sum (Visual Exposure, Distance Zone)
Rioxarray

## Slide 10
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow
(Palmer 2022)
Raster Sum (Visual Exposure, Distance Zone)
Rioxarray

## Slide 11
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
(Palmer 2022)
Raster Sum (Visual Exposure, Distance Zone)
Rioxarray

## Slide 12
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow
(Palmer 2022)
Raster Sum (Visual Exposure, Distance Zone)
Rioxarray

## Slide 13
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow
(Palmer 2022)
Raster Sum (Visual Exposure, Distance Zone)
Rioxarray

## Slide 14
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 15
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 16
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 17
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 18
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 19
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 20
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 21
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 22
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 23
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 24
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 25
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
Geopandas
Rasterio
Shapely
Rasterio
GDAL, Geopandas
Rasterio
Rioxarray
Rioxarray
Rasterio
Rasterio
Geopandas, Rasterio
Rasterio
Geopandas
Reclassify Relative Viewsheds
Wind Turbine Locations
Mean Visual Prominence Raster
GIS Workflow

## Slide 26: Live Demo
Github repository QR code and Jupyter notebook is also available with sample datasets
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography

## Slide 27: Introduction
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography

## Slide 28
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography

## Slide 29: Progress
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography
Planning
Scoping
Visual Impact Assessment
Packaging and Testing
Deployment
Download required datasets for area of interest (AoI)
Perform data engineering, literature review, design Python functions
Create package method for viewshed analysis, buffer analysis and GIS pipeline execution
Test code to handle exceptions and package code
Deploy alpha version for the demonstration

## Slide 30: Future work
Deploy a beta version and improve the code robustly with loggers.
Develop setup.py to accommodates GDAL command line and c-binaries installation across different operating systems (OS).
Develop and debug code using pytests
Add methods to interactive visualization and integrate USGS National Map API, US Wind Turbine Database API to allow higher level abstraction of the analysis.
Optimize and refactor parts of code to achieve coding efficiency and memory usage.
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography

## Slide 31: Credits
Professor JF Palmer, State University of New York College (SUNY)
Travis Williams, National Renewable Energy Laboratory (NREL)
Professor William Gartner, Dept of Geography, University of Wisconsin – Madison
Professor Randy Sincoular, Dept of Geography, University of Wisconsin – Madison
Mahitha Pillodi, Dept of Computer Sciences, University of Wisconsin – Madison
Chinna Subbaraya Siddharth Ramavajjala, MSc GIS & Cartography, Dept of Geography